CJR CONCRETE PUMPING LTD – CONCRETE PUMPING RISK ASSESSMENT

IMPORTANT NOTICE / HEALTH RISK WARNING - ANY PERSON AT RISK MUST BE NOTIFIED OF THE DANGERS DETAILED BELOW BEFORE STARTING ANY CONCRETE PUMPING WORK

| Type of Injury and Cause | Who is at Risk | Risk* | Severity of Injury | How to Prevent |
| --- | --- | --- | --- | --- |
| Concrete splashing into eyes from the end hose | Concrete Gang | H | Low | Goggles must be worn |
| Concrete burns to hands and feet | Concrete Gang | L | Medium to Severe | Gloves, safety wellingtons and barrier cream must be worn |
| Falls or injury to hands, arms, ankles, legs etc from falling on mesh | Concrete Gang / Pump Operator | M | Medium to Severe | Plywood sheets must be provided on mesh in the laying area |
| Back injury due to moving ground pipes | Concrete Gang / Pump Operator | M | Medium to Severe | Use of ropes and good manual handling practices to be adopted |
| High pressure concrete and aggregate going into eyes, face or any exposed skin due to standing or working in front of end hose, or opening up pipe joints when pumping | Concrete Gang Persons working around concreting area General Public | M/H | Severe – can result in loss of sight | Concrete Gang should wear a safety helmet, safety footwear, impervious gloves / gauntlets, high impact goggles and high visibility clothing. Until concrete is flowing smoothly out of the end of the delivery hose, or when a blockage occurs in the boom pipeline, all personnel should remain clear of the delivery hose and placing boom. Under no circumstances should any unauthorised personnel attempt to open the pipeline. All unnecessary personnel including the general public should be kept well away from the concreting area inc lower floors and staircases. |
| Broken limbs, severe injury caused by whiplash of placing hoses. | Concrete Gang | L | Severe or death | Do not kink placing hoses in the ground line. Do not attempt to pump very old concrete or concrete other than a pump mix. . The danger zone is the area around the end hose in which it can strike out. The diameter of the zone is twice the length of the end hose |
| Injury from splash due to blow back from concrete pump hopper | Truck Mixer Drivers | L | Eye injuries possible | Keep hopper full and inform mixer driver of risk |
| Crushing when mixer lorry is backing onto the pump hopper | Person backing truck mixer into pump hopper | L | Severe or death | High visibility clothing must be worn and do not back truck on out of view of mixer driver who will be reversing using mirrors. Keep site personnel out of reversing area. |

*H = High 		M = Medium 			L = Low

CJR Concrete Pumping ABN 50 126 931 413 – PO Box 1226, Maroubra NSW 2035

Plant Risk Assessment

| RA Consultation and Sign off in regard to acceptance of proposed work method and associated responsibilities |
| --- |
| Name | Signature | Date | Name | Signature | Date |
| Christopher Reitano |  |  | Joshua Dagnall |  |  |
| Matthew Bond |  |  | Joshua Gralton |  |  |
| Neil Anscombe |  |  | Charles Ingram-Melsom |  |  |

RA Certification

CJR Concrete Pumping Pty Ltd believes that this Risk Assessment (RA) is compliant with the OHS Act 2000, OHS Regulations 2001, NSW Environmental Legislation, Department of Environment and Conservation “EPA” NSW Regulations, NSW Work Cover Authority Codes of Practice, relevant Australian Standards and applicable statutory requirements, subject to:

a.	ongoing processes of consultation with the review, monitoring and amendment by relevant employee’s in the development of this RA;

b.	amendments to the OHS Act 2000, OHS Regulations 2001, NSW Work Cover Authority Codes of Practice, relevant Australian Standards and applicable statutory requirements; and

c.	lawful requirements of various authorities.

Review changes for next revision of RA: